Change Request

for the update of ISO 20022 financial repository items

- Origin of the request:

A.1 Submitter: nexo A.I.S.B.L.

A.2 Contact person: person(s) Philippe CECE (Philippe.cece@ingenico.com) / Pierre PETITCUENOT (pierre.petitcuenot@e-i.com)

A.3 Sponsors: nexo A.I.S.B.L.

- Related messages:

- StatusReportV08 (catm.001.001.08)

- ManagementPlanReplacementV07 (catm.002.001.07)

- AcceptorConfigurationUpdateV08 (catm.003.001.08)

- MaintenanceDelegationRequestV05 (catm.005.001.05)

- MaintenanceDelegationResponseV03 (catm.006.001.03)

- Description of the change request:

Update DataSetCategory12Code and DataSetCategory13Code by adding the new codesets:

- MediaFile

- SoftwareApplication

- ConfigurationFile

- UploadFile

Create a TerminalPackage element in the AcceptorConfigurationContent8 defined as Group of software packages to transfer to a group of POIComponent of the POI System with multiplicity [0,*] and with type equals to TerminalPackageType1.

Create the message component TerminalPackageType1 defined as Group of software packages related to a group of POIComponent of the POI System with the following message elements:

- POIComponentIdentification defined as Identification of the POI (Point Of Interaction) component with multiplicity [0,*] and with type equals to PointOfInteractionComponentIdentification1.

- Package defined as Chunk of a software package with multiplicity [1,*] and with type equals to PackageType1.

Create the message component PackageType1 defined as Chunk of a software package with the following message elements:

- PackageIdentification defined as Identification of the software packages of which the chunk belongs with multiplicity [0,1] and with type equals to GenericIdentificationXX. (cf another Change Request delaing with the harmonization of GenericIdentification component).

- PackageLength defined as Full length of software package identified through PackageIdentification with multiplicity [0,1] and with type equals to Number.

- OffsetStart defined as Place of the first following PackageBlock, beginning with 0, in the full software package identified through PackageIdentification with multiplicity [0,1] and with type equals to Number.

- OffsetEnd defined as Following place of the last following PackageBlock in the full software package identified through PackageIdentification with multiplicity [0,1] and with type equals to Number.

- PackageBlock defined as Consecutive slices of the full software package identified through PackageIdentification starting with first slice at the place identified with OffsetStart and ending with the last slice at the place identified with OffsetEnd with multiplicity [0,*] and with type equals to IndustryData1.

Update PointOfInteractionComponent9 by :

- Updating POIComponentType5Code to support new codesets:

  - MediaFile

  - SoftwareApplication

  - ConfigurationFile

  - UploadFile

- Adding message element Package defined as Chunk of a software package with multiplicity [0,*] and with type equals to PackageType1

To be filled according to the final suggestion.

- Purpose of the change:

A POI might manage different kind of subcomponent and then provide video or sound support for example. These parameters must be supported by the TMS protocol. Obviously we could use the existing AcceptorConfiguration/DataSet/Content/ApplicationParameters to provide these elements with the message element ParameterFormatIdentifier and Parameters. But many times, these subcomponents must be shared between applications and their management must be kept as easy as possible

Moreover, sometime aiming the application level is not sufficient and a need for lowest levels arose. For instance, we may want to target a sub component of the POI and we may want to download more than 100KBinary.

To solve this, we want to create a new kind of Parameters (TMSProtocolParameters, AcquirerProtocolParameters, MerchantParameters, TerminalParameters, ApplicationParameters, HostCommunicationParameters, SecurityParameters, SaleToPOIParameters) named TerminalModules.

The structure of this parameter will be, as used in an AcceptorConfigurationUpdate message.

Then since it is also important to be able to upload from POI some SoftwarePackage like a LogFile or request some SoftwarePackage, we would like also update the StatusReportBody.

- Urgency of the request:

Necessary.

- Business examples:

Examples illustrating the change request.

- SEG/TSG recommendation:

This section is not to be taken care of by the submitter of the change request. It will be completed in due time by the SEG(s) in charge of the related ISO 20022 messages or the TSG for changes related to the BAH.

| Consider | X | Timing |
| --- | --- | --- |
|  | - Next yearly cycle: 2019/2020 (the change will be considered for implementation in the yearly maintenance cycle which starts in 2019 and completes with the publication of new message versions in the spring of 2020) | X |
|  | - At the occasion of the next maintenance of the messages (the change will be considered for implementation, but does not justify maintenance of the messages in its own right – will be pending until more critical change requests are received for the messages) |  |
|  | - Urgent unscheduled (the change justifies an urgent implementation outside of the normal yearly cycle) |  |  |
|  | - Other timing: |  |

Comments:

| Reject |  |
| --- | --- |

Reason for rejection: